Opcode Table
Operation	PC + 0	PC + 1	PC + 2
rmmov	0x00	RA : RB
mrmov	0x01	RA : RB
rrmov	0x02	RA : RB
irmov	0x03	RA : 00	CONST
add	0x04	RA : RB
sub	0x05	RA : RB
cmp	0x06	RA : 00
jmp	0x07	FLAG : 00	NEW_PC
halt	0x08

Each square in this table represents a single byte in ROM. The colon (X : Y) denotes that X is represented by the leftmost 4 bits, and Y is represented by the rightmost 4 bits, allowing two small codes to be stored in a single byte.

Flags

Flag	Code
AO (always on)	0
LZ (< 0)	1
LE (≤ 0)	2
EQ (= 0)	3
GE (≥ 0)	4
GZ (> 0)	5

Instruction Breakdown

- rmmov RA, RB (2): move data from RA to the memory location whose address is stored in RB
- mrmov RA, RB (2): move data from the memory location whose address is stored in RA to RB
- rrmov RA, RB (2): move data from RA to RB
- irmov RA, CONST (3): move CONST into RA (NOTE: opposite order of X86 irmovq)
- add RA, RB (2): add value in RA to RB
- sub RA, RB (2): subtract value in RA from RB
- cmp RA (2): set flags based on value in RA
- jmp FLAG, NEW_PC (3): if FLAG is set, set PC to NEW_PC

Key: [instr] [args] (byte length)
Note that RA and RB are registers, FLAG is a flag, and NEW_PC and CONST are 8-bit constants.